## Slide 1
Achieving FAIR water quality data exchange thanks to international OGC water standards
Sylvain Grellet – BRGM
09/05/2024 - ESIP - Information Technology and Interoperability Deep Dives
With support from
Hylke van der Schaaf - Fraunhofer IOSB
Katharina Schleidt - DataCove

## Slide 2
Achieving FAIR water quality data exchange thanks to international OGC water standards

## Slide 5
OGC Hydro Domain Working Group ?
Joint OGC – World Meteorological Organization (OMM / WMO) group
  Memorandum of Understanding between OGC - WMO
Target: water data standards => WaterML 2.0 suite : https://www.ogc.org/standard/waterml/
Organizing Interoperability Experiments - (IEs) focused on the water sub-domains
Entry point
https://external.ogc.org/twiki_public/HydrologyDWG/WebHome
Has a Research Data Alliance ‘sister group’
=> ‘Global Water Information Interest Group’
Chairs
    Tony Boston (Australia)
    Silvano Pecora (Italy) – WMO Liaison
    David Blodgett (USA)
http://www.opengeospatial.org/projects/groups/hydrologydwg
Iterative Development

## Slide 6
Group dynamics
A long history of joint activities
    2003 - Earth Systems Science Domain Working Group (DWG)
    2009 - Hydrology DWG
    2011 - Groundwater Interoperability Experiment (IE)
    2011 - Water Information Services Concept Development Study
    2011 - Surface Water Interoperability IE
    2012 - Hydrology Forecasting IE
    2013 - Climate-Hydrology Information Sharing Pilot
    2013 - GroundWater IE2
    2014 - Water ML 2.0 Standards Working Group (SWG)
    2015 - Hydrographic Features SWG
    2015 - Research Data Alliance Global Water Information IG (Hydro DWG sister group)
    2016 - Groundwater SWG
    2017 - Geoscience DWG
    2018 - Environmental Linked Features IE (ELFIE)
    2019 - Borehole IE
    2021 - Second ELFIE (SELFIE)
    2022 - Water Quality IE => on going

## Slide 7
Group dynamics
Un long history of meetings

## Slide 8
Group dynamics
Community
    Members all across the world
    Members from different organization types
      Public administrations
      Public research organizations
      International organization
      Private companies
Some examples
    NR-Can, GSC, USGS, US EPA, CUASHI, SDSC, BRGM, UK CEH, DELTARES, GRDC, BaFG, Univ Tartu, Fraunhofer IOSB, DataCove, NIWA/LAWA (NZ), Federation University (Australia), BoM Australia, CSIRO, …
    WMO, UNESCO, …
    Kisters, 52°N, Aquatic Informatics, …

## Slide 9
A suite of standards
WaterML2.0
    Open and documented
    implemented in WMO Information System and in many organizations : UNESCO, USGS, US EPA, NrCan, NIWA, BRGM, etc…
    And in opensource tools : CUASHI Hydro-Server, Kisters, 52°N etc…
    Updated with a regular contribution from projects involving Hydro DWG partners
9
Part 1 - Timeseries
Part 2 – Ratings, Gaugings and Sections
Part 3 – Surface water features
Part 4 – Groundwater
Part 5 –
Water quality (best practice)
Soon to be updated by the Water Quality IE

## Slide 10
Achieving FAIR water quality data exchange thanks to international OGC water standards
=> The OGC Water Quality Interoperability Experiment

## Slide 11
OGC Interoperability Experiment (IE) ?
OGC Innovation Continuum
Innovation Roadmap
Execution (How)
Innovation Roadmap
Development (What)
We are here

## Slide 12
OGC Interoperability Experiment (IE) ?
We are here

## Slide 13
OGC Interoperability Experiment (IE) ?
Applied research initiative led by OGC members and supported by OGC staff
Most of the time building on the current standards and best practices : the ‘OGC Baseline’ (pushing them to their limits / applying them to a new domain)
Non-OGC member participation is allowed (usually as observers)
In several IEs: GitHub + mailing list + meetings are open
so the ‘observers’ can be really active
Results documented in Engineering Report(s) or other OGC documents and generally used to define new Standardization work.
Some lead to Change Request to the ‘OGC Baseline’
Some to Best Practices in applying it
Some fill in gaps in the ‘OGC Baseline’ proposing document ready for the standardization process: exactly what happened to all the WaterML2.0 series of standards
It’s during the IE that the group decides what the output will be : through experimentation

## Slide 14
OGC Water Quality IE set up
Third time the topic is proposed within the OGC Hydro Domain Working Group
Enough momentum and interest from parties
=> WMO-UNEP-WHO-UNESCO Water Quality workshop in March 2022 (29-31)
https://external.ogc.org/twiki_public/HydrologyDWG/WaterQualityWorkshopSprint2022
=> confirmation of the necessity and organizations interest. Identification of interested parties and IT challenges
Discussion on the best approach => an OGC Interoperability Experiment
Water Quality IE inception
Charter, call for participation, kick-off (20/09/2022)
Co-chairs : Sylvain Grellet (BRGM), Kyle Onda (Lincoln Institute)
Since then :
Starting point : https://github.com/opengeospatial/WaterQualityIE
Weekly meetings
Shared material
  Rolling meeting minutes document,
  One focal point for UML models
  Shared deployment documentation initiated
Note : shared images in that presentation represent Work In Progress currently being tested
The Engineering Report will summarize the group conclusions

## Slide 15
Use Cases identification and work methodology
FoI = Feature Of Interest = the real world feature on which observation is made
Water Quality Use Case prioritisation
  Physical Properties (ex : Temperature, Conductivity), Chemistry
  + Water Quantity as a support to Water Quality
  Out of scope this IE : Biology (taxa observation), Hydro Models, Remote Sensing

## Slide 16
Use Cases identification and work methodology

## Slide 17
FAIR water quality data exchange thanks to international OGC water standards

## Slide 18
Conceptual Modelling
Step 1°/ Express the domain need stemming from the UseCases

## Slide 19
Conceptual Modelling
Step 2°/ Identify the standards in the OGC standard baseline to build on
  2 OGC-WMO water standards : GroundWaterML2.0 & HY_Features
  THE OGC-ISO standard for Observations & Samples : ISO 19156:2023 : Observations, measurements and samples

## Slide 20
Conceptual Modelling
Step 3°/ Express domain needs according to the OGC standard baseline
=> Almost everything is in, just need to agree on how to use it
=> mainly UML “Object diagrams exercise” to document the use of the standards
FROM
TO

## Slide 21
Conceptual Modelling
Backbone to build on: OGC/ISO 19156 (2023) : Observations, measurements and samples (a.k.a OMS)
Credits: Kathi Schleidt, DataCove
https://www.youtube.com/watch?v=bYDSgs2fKLk
Color:
vs.
OMS approach
‘Basic’ approach

## Slide 22
Conceptual Modelling
Backbone to build on: Observations, measurements and samples
Conceptual Observation schema

## Slide 23
Conceptual Modelling
Backbone to build on: Observations, measurements and samples
Conceptual Sample schema

## Slide 24
Conceptual Modelling
Work organised around the identified UseCases
Everything available online : https://umltool.ogc.org/login.php
Follow this path /OGC IEs/ WaterQuality_IE/ WaterQuality_Instance
Ground Water (GW)
GW_InSitu_QuantityObservation
GW_InSitu_QualityObservation
GW_ExSitu_QualityObservation
Surface Water (SW)
SW_InSitu_QuantityObservation
SW_InSitu_QualityObservation
SW_ExSitu_QualityObservation

## Slide 25
Conceptual Modelling
2 modelling patterns
GW_InSitu_QuantityObservation < > SW_InSitu_QuantityObservation
GW_InSitu_QualityObservation < > SW_InSitu_QualityObservation
GW_ExSitu_QualityObservation <> SW_ExSitu_QualityObservation
In situ sensor
Ex situ = Laboratory

## Slide 26
Conceptual Modelling
GW_InSitu_QuantityObservation (water level)
Well
Sensor
Deployment
Hydro Geo Unit
Observing Procedure
Observed
Property
Observation & Result
Spatial Sample
Well & Sensor Observing Capability
In situ sensor

## Slide 27
Conceptual Modelling
GW_InSitu_QuantityObservation (water level)
In situ sensor

## Slide 28
Conceptual Modelling
GW_InSitu_QuantityObservation (water level)
Observation 1°/ & Result
Observation 2°/ & Result
Observation Collection: TimeSeries
TimeSeries Characteristics
In situ sensor

## Slide 29
Conceptual Modelling
GW_InSitu_QuantityObservation (water level)
In situ sensor

## Slide 30
Conceptual Modelling
GW_InSitu_QualityObservation (temperature) => same pattern
In situ sensor

## Slide 31
Conceptual Modelling
GW_InSitu_QualityObservation (temperature) => same pattern
Well
Sensor
Deployment
Hydro Geo Unit
Observing Procedure
Observed
Property
Observation & Result
Spatial Sample
Well & Sensor Observing Capability
In situ sensor

## Slide 32
Conceptual Modelling
GW_InSitu_QualityObservation (temperature) => same pattern
Observation 1°/
& Result
Observation 2°/ & Result
Observation Collection: TimeSeries
TimeSeries Characteristics
In situ sensor

## Slide 33
Conceptual Modelling
GW_InSitu_QualityObservation (temperature) => same pattern
In situ sensor

## Slide 34
Conceptual Modelling
SW_InSitu_QuantityObservation (river flow) => same pattern
Water Quantity Station
Sensor
Deployment
Waterbody
Observing Procedure
Observed
Property
Observation & Result
Spatial Sample
Station & Sensor Observing Capability
In situ sensor

## Slide 35
Conceptual Modelling
SW_InSitu_QuantityObservation (river flow) => same pattern
In situ sensor

## Slide 36
Conceptual Modelling
SW_InSitu_QualityObservation (temperature, pH) => same pattern
In situ sensor
Water Quality Station
Sensor
Deployment
Waterbody
Observing Procedure
Observed
Property
Observation & Result
Spatial Sample
Station & Sensor Observing Capability

## Slide 37
Conceptual Modelling
SW_ExSitu_QualityObservation (ex : Dissolved Oxygen, pH)
Ex situ = Lab
Water Quality Station
Waterbody
Sampling
Material
Sample
SpatialSample
DO Observation & Result
pH Observation & Result
Observing Procedure
Observed
Property
Observing Procedure
Observed
Property

## Slide 38
Conceptual Modelling
SW_ExSitu_QualityObservation (ex : Dissolved Oxygen, pH)
Ex situ = Lab
Water Quality Station
Waterbody
Sampling
Material
Sample
SpatialSample
DO Observation & Result
pH Observation & Result
Observing Procedure
Observed
Property
Observed
Property
Observing Procedure

## Slide 39
Conceptual Modelling
GW_ExSitu_QualityObservation (ex : Nitrate, Arsenic) => same pattern
Ex situ = Lab
Well
Hydrogeo Unit
Material
Sample
Sampling
(sub)
Sampling
Material
(sub) Sample
Nitrate Observation & Result
Arsenic Observation & Result
Observing Procedure
Observing Procedure
Observed
Property
Observed
Property
SpatialSample

## Slide 40
Conceptual Modelling
Ex situ = Lab
GW_ExSitu_QualityObservation (ex : Nitrate, Arsenic) => same pattern

## Slide 41
FAIR water quality data exchange thanks to international OGC water standards

## Slide 42
Which interoperable / FAIR API ?
Available options
OGC WFS/API Features :
  All the identified concepts are Features => could work
  Not tied to a specific semantic/model and quite limited query mechanism on Observation topics
OGC SensorThings API
    Semantics : Already Observations & Measurements compliant
    Powerful query mechanism based on OASIS oData
Decision
Use OGC SensorThings API for Observation, Samples sharing and also a bit of River, Aquifer, Well information => core of the implementation, work presented here
Use OGC WFS / API – Features for pure geospatial features description / Use Cases : River, Aquifer, Well etc…

## Slide 43
OGC SensorThings API?
An OGC standard for exchanging sensor data and metadata
    Historic data & current data
    JSON Encoded
    RESTful
    Adapting OASIS OData URL patterns and query options
    Supporting ISO MQTT messaging
Easy to use & understandable
    Discoverable with only a web browser

## Slide 44
Layman’s terms
Observation
method
Observed
property
Observation
collection
Observation
Feature
of interest
Observer / Sensor / Station
 | "2021-05-07T09:50:00.000Z":"16.79
Sensor type
= Rain gauge
= rainfall time series
= rainfall amount
Sensor intance = The Strasbourg meteo
station
OGC SensorThings API?
= Representative zone
around the station

## Slide 45
Sensor
Observed property
DataStream
Observation
Feature
of interest
Thing
 | "2021-05-07T09:50:00.000Z":"16.79
Sensor type
= Rain gauge
= rainfall time series
= rainfall amount
Historical location
Location
OGC SensorThings API?
Terms from the standard
Sensor intance = The Strasbourg meteo
station
= Representative zone
around the station

## Slide 46
SensorThings API 1.1 – Data Model

## Slide 47
SensorThings live demo
https://airquality-frost.k8s.ilt-dmz.iosb.fraunhofer.de/v1.1
  ~760 000 000 Observations
  ~21 000 Datastreams
  ~5 000 Stations
Docker Quick-Start: https://fraunhoferiosb.github.io/FROST-Server/deployment/docker.html
Full SensorThings API Tutorial https://fraunhoferiosb.github.io/FROST-Server/sensorthingsapi/1_Home.html

## Slide 48
SensorThings API 1.1 – API
 | GET | POST | PATCH | DELETE
v1.1 | Get index |  |  | 
v1.1/Type | Get all of type | Create |  | 
v1.1/Type(id) | Get one of type |  | Update | Delete
v1.1/Type(id)/Entity | Get linked entity |  |  | 
v1.1/Type(id)/EntitySet | Get all linked | Create Linked |  | 
MQTT:
Subscribe
  v1.1/Things
  v1.1/Datastreams(x)
  v1.1/Datastreams(x)/Observations
  etc.
Get Notified
Fully Explorable with just a browser
Composable Responses
Powerful filtering
HTTP:
https://datacoveeu.github.io/API4INSPIRE/sensorthingsapi/1_Home.html

## Slide 49
Fancy Queries
All data for a map: v1.1/Things?
$select=id,name,description,properties&
$top=10&
$filter=properties/countryCode eq 'HR'&
$expand=
Locations($select=location),
Datastreams(
$select=id,name,unitOfMeasurement;
$expand=
ObservedProperty($select=name),
Observations(
$select=result,phenomenonTime;
$orderby=phenomenonTime desc;
$top=1)
)
Link

## Slide 50
Physical model -> Mapping to OGC SensorThings API
Map matching concepts
  Monitoring Facility → Thing + Location
  Observed Property → ObservedProperty
  Observation Collection → Datastream
  Observation → Observation
  Observer → Sensor
  Sample → FeatureOfInterest
Add missing Classes
  SampledFeature (River)?
  Deployment?
  Sampler?
  ObservingProcedure?

## Slide 51: SensorThings API 1.1 – Water Quality
Sample +Location +Sampling
Host
Time series
River? (SampledFeature)
Deployment?
Sampler?
ObservingProcedure?

## Slide 52: STA 1.1 WQ-IE – Sensor Extensions
Extending the Sensor
Deployment
ObservingProcedure
OMS addition

## Slide 53: STA 1.1 WQ-IE – Sampling
Adding Sampling from OMS
Sampling
Sampler
SamplingProcedure
OMS addition

## Slide 54: STA 1.1 WQ-IE – Features
Adding the River as Feature and linking a time series
FeatureType
Datastream → UltimateFeatureOfInterest
OMS addition

## Slide 55: STA 1.1 WQ-IE – Relations
Relating Features to other Features
RelatedFeature
RelationRole
The same for:
RelatedThing
RelatedDatastream
RelatedObservation
Relation extension

## Slide 56: STA 1.1 WQ-IE
Full data model
Still v1.1 compatible
Paving the way to STA 2.0
STA 1.1
OMS addition
Relation extension

## Slide 57
FAIR water quality data exchange thanks to international OGC water standards

## Slide 58
Implementation
Who
    Water Quality IE members USGS, USEPA, DataStream (Canada), BRGM, BaFG (Unesco Gems water), Fraunhofer
    EU Water4All project partners
  Ex : Danish DEP, ISPRA, Fraunhofer, VITO etc…
    EU GSEU project partners
  Many EU geological surveys
What
    FROST Data Model Plugin https://github.com/hylkevds/FROST-Server.Plugin.WaterQualityIE
    Docker Image https://hub.docker.com/r/hylkevds/frost-http-waterquality

## Slide 59
Implementation
How
    Documentation being written Google doc for now, will be moved to the GitHub when more mature https://docs.google.com/document/d/1Oqjxrz8uY_Q9OKBwEM2ZufrCEnlYvA4vWIIJSiMyGT4/edit
Demo endpoints
    Open Free-For-All Service (no data yet) https://ogc-demo.k8s.ilt-dmz.iosb.fraunhofer.de/FROST-WaterQuality/v1.1/
    USGS endpoint (work in progress) Data: https://wqp.wqie.internetofwater.app/FROST-Server/v1.1 Map: https://wqp.wqie.internetofwater.app/ Map: https://wg-brgm.k8s.ilt-dmz.iosb.fraunhofer.de/servlet/is/211/
    Also tested in QGIS SensorThings API Plugin

## Slide 60
Implementation
It works !
Surface water quality
USGS – Internet of Water US
Surface water quality
France - Germany

## Slide 61
Implementation
French & German Data
1 Map

## Slide 62
Implementation
French & German Data
1 Map

## Slide 63
FAIR water quality data exchange thanks to international OGC water standards
Conclusion

## Slide 64
Landing the Interoperability Experiment
When
    Current target => OGC Member Meeting in June 2024 (OGC Hydro DWG session)
What
    Demo based on the implementation feedback
    + draft Engineering Report
  summarizing the findings from the IE
  and proposing next steps. Ex : adoption of a Best Practice for Water Quality data exchange Water ML2.0 Part 5 and (potentially) a revision of WaterML2.0 Part 1 : TimeSeries

## Slide 65
Steps after the Interoperability Experiment
Finalize a Best Practice for Water Quality data exchange Water ML2.0 Part 5 and start a draft revision of WaterML2.0 Part 1 : TimeSeries (to align with OMS and ST API )
Work on shared ‘controlled’ vocabularies
    Observed Property (? using I-ADOPT ? ), Observing Procedure, …
Current UseCases
    More implementations : La Plata basin countries (through WMO), more Water4All and GSEU project partners
Address the other UseCases
    Out of scope this IE : Biology (taxa observation), Hydro Models, Remote Sensing
    Enough material for a WQ IE 2 

## Slide 66
Some hindsight on the effort
How the new “Observations, measurements and samples (OMS) ” is meaningful to the Interoperability Experiment ?
    Most of what is needed semantically is already within the OGC semantic baseline : OMS + OGC WaterML2.0 part 3 (HydroFeatures) and part 4 (GroundWaterML 2.0)
    OGC SensorThings API 1.1 being already Observations & Measurements compliant we just needed to add the missing elements to make it OMS compliant (ex : MaterialSample and some others)
    This is now embedded in SensorThings 2.0 working draft (revision ongoing)

## Slide 67
Some hindsight on the effort
How the new “Observations, measurements and samples (OMS) ” is meaningful to the Interoperability Experiment ?
=> No need to reinvent the wheel, just use the available standards and document it

## Slide 68
Some context supporting this work
Some supporting national /EU projects from our end (both running now)
  French Research project, 53 Million €, 10 years
  https://www.onewater.fr/en (ANR project : 22-PEXO-0009)
  Many domain objectives including FAIR (interoperable) Water Data Exchange
  EU joint research partnserhip
  https://www.water4all-partnership.eu/
  31 countries, 7 years, 81 Million € for the 2 years.
  Many domain objectives including FAIR (interoperable) Water Data Exchange
Your project could join the effort
  join the OGC Hydro DWG discussions

## Slide 69
Thank you
s.grellet@brgm.fr

## Slide 70
Thank to
Kathi Schleidt
Kathi@DataCove.eu
Hylke van den Schaaf
hylke.vanderschaaf@iosb.fraunhofer.de